## Slide 1
Leak
Management
For Your Compressed Air System
Proven and innovative
measuring technology
for compressed air and gases
Robin Gillis / Thomas Blessing
Business Developer Leak Detection / Product Manager Leak Detection
CS INSTRUMENTS

## Slide 2
AGENDA
LEAK MANAGEMENT to reduce your energy costs
introduction
Why start finding leaks?
How to find leaks?
Document and manage your savings
Insights in leak and energy management
Notes: AGENDA

## Slide 3
  Robin Gillis
  Business Developer Leak Detection
  Thomas Blessing
  Product Manager Leak Detection
introduction
Meet The hosts
  Questions?
  Ask in chat
Notes: Quick introduction
Left is the webinar speaker
Right is the support
Questions can be asked in chat,
Answer (relevant) questions during overview slides in between topics or at the end of the presentation

## Slide 4
introduction
a brief CS HISTORY
2002 Founded by Christian Schuldt († 2014) and Wolfgang Blessing
Expert in compressed air and expert in dewpoint sensors
In 2002 dew-point was the most measured value after pressure on compressed air
2005 Flow sensors specifically for compressed air
  No specific flow meter at that time for compressed air
2006 Leakage measurement => 2017 leakage management
Our goal: to help you to save energy and improve your productivity by monitoring your compressed air system.
Reduce
Save
Productivity
Insights
Sustainability
FA200 dewpoint sensor (2003 – 2007)
Notes: Founded in 2002 – Started with dewpoint sensors
Expand to more instrumentation

## Slide 5
Location North | Harrislee (Schleswig-Holstein)
Location South | VS-Tannheim (Baden-Württemberg)
Headquarters
Subsidiaries
GERMANY
FRANCE
AUSTRIA
SOUTH AFRICA
SWITZERLAND
ITALY
USA
BENELUX
SPAIN
TURKEY
SWEDEN / NORWAY
CHINA
Worldwide partners
INDONESIA
INDIA
POLAND
250 Employees worldwide
Notes: ALL MADE IN GERMANY
Origin in south office – Research and production
Logistics and own calibration in north office
Many subsidiaries and worldwide partners

## Slide 6
Efficiency measurement of compressors
Quality monitoring according to ISO 8573-1
Flow-/ Consumption management
Leakage Management
Generation
Consumption
70% Compressed air
27% Other gases like:
  N2; CO2; H2; N2O; CH4; Ar; O2, ...
2% Humidity sensors
1% Steam
introduction
measuring solutions
Notes: 70% of our market is compressed air
1 Efficiency measurement
2 Quality monitoring
3 Flow management
4 Leak Management
All combines to energy savings and quality verification

## Slide 7
45 dB
€ 10,1/y
introduction
Leak detection history
LD500
2013
LD300
2006
LC600
2025
Notes: CS has been developing leak detectors for 20 years
LeakCam is most recent and most advanced

## Slide 8
AGENDA
LEAK MANAGEMENT to reduce your energy costs
introduction
Why start finding leaks?
How to find leaks?
Document and manage your savings
Insights in leak and energy management
Notes: INTRO INTO WHY YOU SHOULD START FINDING LEAKS

## Slide 9
WHY START FINDING LEAKS?
Compressed air cost
Illustrative image
105 kW * 8500 h/y * €0,20 / kWh
Energy cost / year = €178.500
90 kW compressor
105 kW
8500 h / year
€0,20 / kWh
Notes: EXPLAIN POTENTIAL SAVINGS
Example situation, not 100% realistic
!!!(EDIT ENERGY PRICE FOR YOUR REGION)!!!

## Slide 10
WHY START FINDING LEAKS?
Compressed air cost
Chart: 
| 1e kwartaal | 2e kwartaal | 3e kwartaal
Verkoop | 80 | 11 | 9
Energy cost
Initial purchase
Maintenance
80 %
11 %
9 %
On average, compressed air makes 5 - 30% of plant energy costs
Notes: Total cost of a compressor over its life is
80% energy cost
11% purchase and installation
9% maintenance

## Slide 11
WHY START FINDING LEAKS?
Compressed air cost
Illustrative image
105 kW * 8500 h/y * €0,20 / kWh
Energy cost / year = €178.500
Total cost / year =
€223.125
90 kW compressor
105 kW
8500 h / year
€0,20 / kWh
Notes: €178500 is only energy cost (80%)
Total yearly cost = +20%

## Slide 12
Effective use ± 80%
Leaks ± 15%
Potential savings
WHY START FINDING LEAKS?
Compressed air cost
Inefficiencies
Energy cost / year = €178.500
Potential savings / year = €35.700
90 kW compressor
Illustrative image
Notes: Compressed air is expensive (energy costs)
Aim to use it effectively
On average only 70-80% is used effectively
Potential saving of 20-30%
20% of our example energy cost is €35700 / year
ENERGY COST REDUCTION AND CO2 REDUCTION

## Slide 13
Effective use ± 80%
Leaks ± 15%
WHY START FINDING LEAKS?
Compressed air cost
Inefficiencies
Measure your losses
Potential savings
90 kW compressor
Illustrative image
Notes: Measure flow on main pipe
Reveal potential savings for your plant
THIS EXAMPLE IS COMPRESSOR ONLY
REALISTIC SITUATION HAS MORE INEFFICIENCY LOSSES DUE TO DRYERS, FILTERS,… here we only measure the leaks AFTER all of our air treatment
Total losses can easily be 30-40%

## Slide 14
100l/s
130l/s
40l/s
85l/s
55(60)kW Oil-Free compressor – 144l/s or 8,6m3/min max
Geuze brewery in Belgium
WHY START FINDING LEAKS?
Measure your losses
Production
Operating time
Monday - Friday
6 - 22h
6 – 22h
14
Notes: FLOW SENSOR INSTALLED IN BREWERY IN BELGIUM
(Describe graph before advancing)
Operation runs from Monday-Friday, 6-22h
Green square is normal operation time and air usage

## Slide 15
100l/s
130l/s
40l/s
85l/s
Normal use
Exceptional use?
Poor system management ?
Geuze brewery in Belgium
WHY START FINDING LEAKS?
Measure your losses
Leaks
55(60)kW Oil-Free compressor – 144l/s or 8,6m3/min max
15
Notes: Within the green square, mark normal use
High peaks are exceptional use or poor management
HIGHLIGHT constant use of 40l/s EVERY DAY – EVERY HOUR => LEAKS

## Slide 16
WHY START FINDING LEAKS?
Measure your losses
40l/s or 2,4m3/min @ 9kWh/m3/min = 21,6kWh
0,2€/kW * 21,6kWh => 4,32€/h * 8760h = 37.843€/y
40 l/s * 9kWh/m³ = 21,6kWh
0,2 €/kWh => 4,32 €/h
Leak cost =
€37.843 / year
55 kW compressor
16
Notes: 40l/s or 2,4m3/min at 9kW/m3/min = 21,6kW
Multiply leak loss rate by energy/volume => energy loss
Multiply energy loss by energy cost => yearly leak cost
Yearly leak cost = one nice car/year

## Slide 17
WHY START FINDING LEAKS?
Measure your losses
Capacity savings:
40l/s leak losses /
144l/s max capacity
Load reduction =
27,7%
55 kW compressor
17
40l/s or 2,4m3/min @ 9kWh/m3/min = 21,6kWh
0,2€/kW * 21,6kWh => 4,32€/h * 8760h = 37.843€/y
Notes: Fixing leaks frees up compressor load
40 l/s leak losses divided by 144l/s max capacity of the compressors = 27% capacity freed up

## Slide 18
+
>
Leaks
LeakCam600
WHY START FINDING LEAKS?
System management
37 kW
55kW
Better than
Fix leaks before upsizing compressors
18
Notes: Fix leaks before upsizing compressors
Better to have a smaller compressor and manage leaks
Than have a large compressor to compensate for +30% losses (or more)

## Slide 19
AGENDA
LEAK MANAGEMENT to reduce your energy costs
introduction
Why start finding leaks?
How to find leaks?
Document and manage your savings
Insights in leak and energy management
Notes: Now that potential savings are clear
How can you find these compressed air leaks?

## Slide 20
How To find leaks?
Compressed air leaks
Try to find the leaks!
Notes: Some leaks are easy to spot, water is very visible
In an industrial setting there are:
Many systems and components
A lot of noise
Hard to access some areas (safety for moving parts)
Using human ear or leak spray is possible, but very hard and slow

## Slide 21
How To find leaks?
Ultrasound principle
Rapid expansion and increase in velocity causes vibration.
Leak turbulence generates ultrasonic sound, often measured around 40 kHz.
Compressed air
Steam
Vacuum
Any compressed gas (CO2, nitrogen, refrigerants,…)
Notes: We can detect leaks using ultrasound principle
High pressure escaping through a small opening creates a flow increase and turbulence (created at Δp 0,3 bar)
Most of this sound cannot be heard by the human ear
Ultrasound can be detected with specialized microphones

## Slide 22
How To find leaks?
Leakcam 600
Visualise your leaks
64 Ultrasonic microphones
HD camera
Power Beam Forming
Calculates leak costs
Document leaks
45 dB
€ 10,1/y
Notes: LeakCam600 has 64 ultrasound microphones and a high quality camera
Visualise leaks
Calculate leak size and cost
Document with photo

## Slide 23
How To find leaks?
Leakcam 600
Visualise your leaks
Scan for ultrasound
Measure volume
Laser for distance
Calculate position, cost and size
45 dB
€ 10,1/y
Notes: How it works?
64 microphones all measure separately in a window.
Location of leak is determined by referring to other microphones
Laser to measure distance
Calculate position, volume and distance to leak for size and cost

## Slide 24
How To find leaks?
Power Beam Forming
LeakCam600
LD500 UltraCam
Notes: The strength of power beam forming is in the calculation algorithm
64 mics can make an image. But only loudest leak can be picked up
To find more leaks that differ in size, double or triple microphones are required for slightly better result
CS focuses on powerful calculation over increasing microphones. We have better imaging and larger range with less microphones compared to other alternatives
This reduces price of leakcam while still offering the highest dynamic range and top quality imaging

## Slide 25
How To find leaks?
Leakcam 600
Power Beam Forming
12dB Dynamic range
Detect up to 6 leaks in one image
Large dynamic range to see all leaks
Standard Beam Forming
3dB Dynamic range
Only see the largest leak
Low dynamic range
Notes: With power beam forming => see up to 6 leaks at once. Even if they are much different in size
Standard beam forming => small dynamic range => only detect largest leak, miss small leaks
Technician will fix a leak, after repair he will discover another leak
With LeakCam, find all leaks at once

## Slide 26
How To find leaks?
Power Beam Forming
LeakCam600
Detect both leaks
Large dynamic range
Calculate leak rate and cost
Previous auditor
Only see the largest leak
Low dynamic range
No leak rate or cost
63 dB
€ 37,4/y
69 dB
€ 98,7/y
?? dB
€ ??/y
Notes: Practical example during leak audit preformed with LeakCam
I detect a leak that was marked by previous auditor, and another smaller leak very close
Previous auditor missed smaller leak
No leak size or cost on marked leak, no documentation, no priority for repair, no data on energy saving

## Slide 27
How To find leaks?
LeakCam 600
Unique traits of the LC600
+20m range for medium leak size
Wide and clear view camera
Easy and quick cost calculation
Automatic filtering
Customisable 2-130 kHz frequency range
Notes: 20+ meter of realistic range
Quickly find leaks with clear and wide view camera
Anyone can use without training => Automatic filtering
Customisable 2-130kHz frequency range for extremely high disturbance situations

## Slide 28
How To find leaks?
High-noise environment
Automatic filtering helps detect leaks in noisy plants
Notes: Even in very noisy envoirements, small leaks can be found thanks to excellent automatic filtering
Vacuum installation (small leaks), loud environment (technician wears hearing protection)
LeakCam detects leak created for testing and second leak technician was not aware of

## Slide 29
How To find leaks?
LeakCam 600
Unique traits of the LC600
5”HD display for clear image
Interchangeable battery (8h use)
Lightweight and durable
Ergonomic design & holster
Notes: LeakCam has very good ergonomics thanks to large clear display
Use all day with 2 interchangeable batteries
Lightweight and durable design, pair with holster for scaling ladders or very long use

## Slide 30
How To find leaks?
For any compressed gas application
Compressed air
Vacuum
Steam
Natural gas
CO2
Refrigerants
Nitrogen
Helium
Hydrogen
Methane
…
Notes: Accurately detect leaks on many applications
Refrigeration chiller (left)
Natural gas (top right)
Vacuum (bottom right)
And many many more

## Slide 31
How To find leaks?
More leak detectors
LD450
Basic leak detector
LD500
Size & cost calculation
Documentation
LD500 UltraCam
Basic imaging
Size & cost calculation
Documentation
Notes: Our complete range of leak detectors
LD450
Basic, budget option, audio only, no documentation
LD500
Camera for assistance and documentation, calculate leak size and cost
ULTRACAM
Basic imaging, documentation, size and cost calculation

## Slide 32
How To find leaks?
Leakcam specialty
Standard zoom
2x zoom
Notes: Leakcam excels at precisely finding leaks at long range. Perfect for inaccessible zones
Zoom up to 8x

## Slide 33
How To find leaks?
Leakcam specialty
Standard zoom
2x zoom
Notes: Zoom up to 8x to closely inspect which part is leaking. Even when physically getting closer is not an option

## Slide 34
How To find leaks?
Leakcam specialty
Long range
High accuracy
Notes: Leakcam excels at precisely finding leaks at long range. Perfect for inaccessible zones due to moving parts and fenced off areas

## Slide 35
AGENDA
LEAK MANAGEMENT to reduce your energy costs
introduction
Why start finding leaks?
How to find leaks?
Document and manage your savings
Insights in leak and energy management
Notes: Now we know how to find leaks
To fix the leaks and reduce energy cost, we need to document and manage the leaks

## Slide 36
Document and manage your savings
Leak Documentation
Find the leak
Document the leak
Assign priority
Fix the leak
Verify the repair
Notes: 1st step is to find leak
2nd step is to document the leak. Extra info can be entered on leak detector and afterwards in software (location, description, repair steps,…)
3rd step is to assign priority for repair
4th step is to fix the leak
5th step is to check repair is ok

## Slide 37
Document and manage your savings
Leak Documentation
Leak Reporter V2
Fast reporting
Professional documentation
Practical repair workflow
Notes: Using our leak detectors and software
Fast and easy reporting
Make professional leak reports and documentation
Manage leaks for repair

## Slide 38
Document and manage your savings
Leak Documentation
Edit parameters
Add repair information
Select repair priority
Notes: 1 On leak detector or in software, edit all parameters
2 Add repair information (location, description, repair steps,…)
3 assign repair priority

## Slide 39
Document and manage your savings
Leak Documentation
1 hour audit
€5000+ leaks found
Notes: Example leak report, I was on this site for 30 minutes and found 52 leaks. Total cost of +€5000 (can use personal case)
Leaks can be filtered and sorted however you like
Highest > lowest cost (can be useful for assigning repair priority)
Total cost is calculated for all leaks

## Slide 40
Document and manage your savings
Leak Documentation
Manage your leaks and savings in the software or cloud
Work on ISO 50001
Notes: Save and manage all leaks in software
Document repairs
Work towards ISO50001 => reduce energy cost, reduce CO2 emissions

## Slide 41
Document and manage your savings
Leak Documentation
Export to PDF or Excel
Nr. | Date | Detected by | Building | Machine | Input value | Leakage detection device
255 | 4/30/2026 |  |  |  | 88,32 | Flow rate [l/min]
237 | 4/30/2026 |  |  |  | 74,9232 | Flow rate [l/min]
256 | 4/30/2026 |  |  |  | 28,655432 | Flow rate [l/min]
254 | 4/30/2026 |  |  |  | 22,07515 | Flow rate [l/min]
249 | 4/30/2026 |  |  |  | 11,2986555 | Flow rate [l/min]
292 | 5/5/2026 |  |  |  | 9,035373 | Flow rate [l/min]
216 | 4/21/2026 |  |  |  | 8,188495 | Flow rate [l/min]
247 | 4/30/2026 |  |  |  | 6,9150143 | Flow rate [l/min]
236 | 4/30/2026 |  |  |  | 6,425377 | Flow rate [l/min]
253 | 4/30/2026 |  |  |  | 5,794931 | Flow rate [l/min]
251 | 4/30/2026 |  |  |  | 5,273667 | Flow rate [l/min]
281 | 4/30/2026 |  |  |  | 5,2446136 | Flow rate [l/min]
280 | 4/30/2026 |  |  |  | 5,207753 | Flow rate [l/min]
257 | 4/30/2026 |  |  |  | 4,8158426 | Flow rate [l/min]
248 | 4/30/2026 |  |  |  | 4,578567 | Flow rate [l/min]
275 | 4/30/2026 |  |  |  | 4,1670275 | Flow rate [l/min]
258 | 4/30/2026 |  |  |  | 4,0971985 | Flow rate [l/min]
260 | 4/30/2026 |  |  |  | 3,6970916 | Flow rate [l/min]
234 | 4/30/2026 |  |  |  | 3,098467 | Flow rate [l/min]
277 | 4/30/2026 |  |  |  | 3,0154214 | Flow rate [l/min]
241 | 4/30/2026 |  |  |  | 2,5226169 | Flow rate [l/min]
268 | 4/30/2026 |  |  |  | 2,457378 | Flow rate [l/min]
235 | 4/30/2026 |  |  |  | 2,4214761 | Flow rate [l/min]
226 | 4/23/2026 |  |  |  | 1,4531308 | Flow rate [l/min]
278 | 4/30/2026 |  |  |  | 1,4525505 | Flow rate [l/min]
279 | 4/30/2026 |  |  |  | 1,3375479 | Flow rate [l/min]
240 | 4/30/2026 |  |  |  | 1,2145209 | Flow rate [l/min]
246 | 4/30/2026 |  |  |  | 0,6685253 | Flow rate [l/min]
232 | 4/30/2026 |  |  |  | 0,65 | Flow rate [l/min]
238 | 4/30/2026 |  |  |  | 0,65 | Flow rate [l/min]
239 | 4/30/2026 |  |  |  | 0,65 | Flow rate [l/min]
242 | 4/30/2026 |  |  |  | 0,65 | Flow rate [l/min]
252 | 4/30/2026 |  |  |  | 0,65 | Flow rate [l/min]
261 | 4/30/2026 |  |  |  | 0,65 | Flow rate [l/min]
262 | 4/30/2026 |  |  |  | 0,65 | Flow rate [l/min]
263 | 4/30/2026 |  |  |  | 0,65 | Flow rate [l/min]
266 | 4/30/2026 |  |  |  | 0,65 | Flow rate [l/min]
270 | 4/30/2026 |  |  |  | 0,65 | Flow rate [l/min]
273 | 4/30/2026 |  |  |  | 0,65 | Flow rate [l/min]
274 | 4/30/2026 |  |  |  | 0,65 | Flow rate [l/min]
276 | 4/30/2026 |  |  |  | 0,65 | Flow rate [l/min]
221 | 4/23/2026 |  |  |  | 0 | Flow rate [l/min]
243 | 4/30/2026 |  |  |  | 0 | Flow rate [l/min]
244 | 4/30/2026 |  |  |  | 0 | Flow rate [l/min]
245 | 4/30/2026 |  |  |  | 0 | Flow rate [l/min]
259 | 4/30/2026 |  |  |  | 0 | Flow rate [l/min]
264 | 4/30/2026 |  |  |  | 0 | Flow rate [l/min]
267 | 4/30/2026 |  |  |  | 0 | Flow rate [l/min]
269 | 4/30/2026 |  |  |  | 0 | Flow rate [l/min]
271 | 4/30/2026 |  |  |  | 0 | Flow rate [l/min]
272 | 4/30/2026 |  |  |  | 0 | Flow rate [l/min]
282 | 4/30/2026 |  |  |  | 0 | Flow rate [l/min]
Notes: Manage all date in software
Alternatively,
Leak reports can be generated in pdf or exported to excel

## Slide 42
Document and manage your savings
prioritise Economical leaks
Leak rate = 22,7 l/m
Leak cost = € 348,08 / year
Repair under pressure = Yes
Repair cost = € 1,5
Repair time = 1 minute
Notes: Now that you can find and document leaks
It’s important to prioritise your leaks for repair.
Example here, pneumatics are oversized for future expansion
Active compressed air lines are poorly sealed, 4 leaks are found.
VERY HIGH LEAK COST
REPAIR UNDER PRESSURE IS POSSIBLE (no system interruptions)
VERY LOW REPAIR COST AND EFFORT

## Slide 43
Document and manage your savings
prioritise Economical leaks
Leak rate = 5,8 l/m
Leak cost = € 71,8 / year
Repair under pressure = No
Repair cost = € 500
Repair time = 2 hours
Notes: Another leak in same plant
Relatively small leak on main compressor line on ceiling
-low leak reate and cost
-no repair under pressure (no valves, system must shut down)
-high repair cost due to lift needed and work hours
Document leak and plan for fix during yearly maintenance shut down

## Slide 44
Document and manage your savings
prioritise Economical leaks
Repair cost
Energy cost
1
2
2
3
Economical & High-risk leaks
€
Notes: Graph with repair cost in relation to energy cost
1st example is priority repair due to high cost and cheap fix
Dangerous and flammable leaks are also priority
2nd example is not priority due to low cost and difficult repair
Manage and plan repair during yearly maintenance shut down

## Slide 45
Document and manage your savings
Efficient energy management
Track energy savings
Calculate CO2 savings
Optimise energy use
Notes: Finding, documenting and repairing leaks saves energy costs
Software calculates CO2 reduction
Optimise energy use
Become ISO50001 certified

## Slide 46
AGENDA
LEAK MANAGEMENT to reduce your energy costs
introduction
Why start finding leaks?
How to find leaks?
Document and manage your savings
Insights in leak and energy management
Notes: More insights in leak and energy management

## Slide 47
More insights
Insights in compressed air management
Effective use ± 80%
Leaks ± 15%
Inefficiencies
Potential savings
Notes: Go back to brewery example. Place flow meter to see trends and predict leak losses

## Slide 48
P
Compressor
2
Compressor
1
Compressor
3
Dryer
Dryer
VA 520
VA 520
VA 550
To division 1
To division 2
To division 3
More insights
Flow Sub-metering
Track usage
VA 500
Notes: Same concept, place flow meters for each production line/step to get clear view in plant usages
Every sector becomes responsible for compressed air use, find leaks and inefficiencies more accurately
CS has many different flow sensors, wet and dry
For many different gases

## Slide 49
VD 500
Compressor
Dryer
Wet
Dry
VA 500
Flow
DS 500
FA 510
Dewpoint
Thermal mass
Clamp-on
Ammeter on electricity in
More insights
Performance measurement
Wire to Air
PM 5110
Differential pressure
Flow
Data
Notes: We also offer performance measurements
Wire to air + wet flow meter directly after compressor => compressor performance
Data recorder for trends and data logging

## Slide 50
Pre-
filter
Compressor
Dryer
Filter
Oil injected
Filter
Refrigeration
Dryer
Compressor
Dryer
filter
filter
Environment
filter
filter
filter
Filter
Filter
filter
Filter
ACF
Residual Oil
Dewpoint
DS 500
Data recorder
FA 510
Activated carbon filter
Dry vessel
More insights
Quality measurement
PC400
FA510
IAC 500
OC500
Particles
Notes: Mobile and continuous quality measurements
Dew point
Oil check
Particle counter point of use

## Slide 51
71 types / +5000 variants / 310 options
Quantity and quality management
Dew-point measurement
Flow measurement
Oil and particles measurement
VA 520
Chart recorder / Data management
Leakage Management
DS 400
OIL-Check 500
Mobile measurement
DP500
DS 500
UltraCamLD 500
30 microphones
Particle counter 400 & data logger DS500

## Slide 52
r.gillis@cs-instruments.com
Thomas Blessing
Product Manager Leak Detection
t.blessing@cs-instruments.com
info@cs-instruments.com
+49 7705 978 990 (en / de)
Proven and innovative measuring
technology for compressed air and gases
Leakage
measurement
Data
management
Particles
measurement
Residual Oil
measurement
Robin Gillis
Business Developer Leak Detection
Flow
sensors
Temperature & Pressure
Notes: Questions can be answered here. Good/relative questions asked in chat can also be answered in between topics.
Fake questions in case no one responds:
What’s the max range of leakcam? Some say 100m? => We use a realistic max range of 20m for medium sized leaks. Really large leaks can be detected at great distances. For example someone using a sand blaster or power washer. It’s more of a marketing trick to say 100m.
Will the leakcam work in my noisy factory? => yes the leakcam has advanced automatic filtering for easy use. There are also preset filters and a fully customisable range if you want to filter out specific ranges
Why only 64 microphones when xxx has 100+? => Refer to slide 24. There’s a balance to be picked between adding microphones for slightly better image or improving calculation and processing power to get a higher dynamic range. Many alternatives to leakcam have more microphones but do not have better imaging or a larger range. LeakCam is almost unique in it’s broad range. Less microphones also greatly reduces the price.
Why 2-120kHz range when xxx has 140kHz or more? => Typical leak frequency range is around 40kHz, in some situations or applications it can range from 10-80kHz but beyond 100kHz there is almost no relevant readings. Only in exceptional cases will you find anything relevant beyond 100kHz.